## Slide 1
Dakota Benjamin, Geospatial Developer, Cleveland Metroparks
@dakotabenjammin
Stephen Mather, GIS Manager, Cleveland Metroparks
@smathermather

## Slide 2
OpenDroneMap is an open source toolkit for aerial drone imagery.
It is modern photogrammetry - fully automated matching, digital surface modelling, and mosaicking

## Slide 3: Presentation Layout
Practical overview
Anatomical breakdown
Future Plans

## Slide 4: Origins
Computer Vision
Stereo views of the world
Notes: OpenDroneMap originates from Computer Vision, i.e. how do we enable computers to navigate and understand the world.
It depends on stereo vision much like we do to make sense of the world in 3D

## Slide 5: Photogrammetry Process
Structure from Motion
Point Cloud Densification
Poisson Surface Reconstruction
Multi-View Stereo Texturing
Orthophoto Generation

## Slide 6: Structure from Motion
Matches features extracted from images with overlap
Credit: Michelle Tobias

## Slide 7: Point Cloud from Matching
Notes: (Photogrammetrically Derived Point Cloud)

## Slide 8: Dense Point Cloud from finding all matches

## Slide 9: Mesh
Notes: Uses the Point Cloud Library (PCL), followed by mesh decimation

## Slide 10: Mesh
Notes: Uses the Point Cloud Library (PCL), followed by mesh decimation

## Slide 11: Texturing

## Slide 12: Orthophoto Generation

## Slide 13: Installation
There are many ways to install ODM:
  Natively using Ubuntu 14.04 or later (or with Virtual Machine via vagrant)
  MacOS or Windows, by installing Docker (not covered today)
  With a Web-based GUI called WebODM (functional, but limited and currently in heavy development)

## Slide 14: Installation and Usage
Download:
  V0.2 Release: https://github.com/OpenDroneMap/OpenDroneMap/releases/download/v0.2/OpenDroneMap-v0_2.zip
  Latest Development: (git)
    git clone https://github.com/OpenDroneMap/OpenDroneMap.git
  Or download link above (sans “.git”)
Install
  $ ./configure.sh

## Slide 15: Installation (cont.)
3. Set environment variables
  Open “~/.bashrc in your favorite editor and append:
    export PYTHONPATH=$PYTHONPATH:/your/path/OpenDroneMap/SuperBuild/install/lib/python2.7/dist-packages
    export PYTHONPATH=$PYTHONPATH:/your/path/OpenDroneMap/SuperBuild/src/opensfm
    export LD_LIBRARY_PATH=$LD_LIBRARY_PATH:/your/path/OpenDroneMap/SuperBuild/install/lib
  Replace “/your/path/” appropriately
  Log out/in again

## Slide 16: Running OpenDroneMap
Project Setup:
  Create a project folder and places your images in an "images" directory:
  |-- /path/to/project/
  |-- images/
  |-- img-1234.jpg
  |-- ...
Then run:
    python run.py -–project-path /path/to/project

## Slide 17: Inputs / Outputs

## Slide 21: OpenDroneMap: Future
Scalability
  Reduce memory footprint
  Data Partitioning
Analysis
  Add automated DEM extraction
  Classification
Mesh improvements
Testing

## Slide 22: WebODM: Future
DEM display
Volumetric Measurements
Mission Planning
Mobile App for autonomous flight
QGIS integration