## Slide 1
Corey Snipes
Twomile Heavy Industries, Inc.
UCANR DroneCamp - June 24, 2020
Open Source Data Processing With

## Slide 2: Agenda
Background
How ODM Works
Use Cases
Using ODM
(Start Hands-on Processing)
Outputs
Pitfalls, Future Direction
Learning Resources
QA/Break
Hands-On Exercises

## Slide 3: Background

## Slide 4: About Me
Senior Software Engineer, Mosaic ATM
Board President, North Coast Drone Alliance
Drone industry participant ~5 years
Part 107 Remote Pilot (<1 year)
Contributor in the OpenDroneMap ecosystem

## Slide 5: Why Open Source
FOSS is popular in academic and research settings, but why?
Accessible to orgs and programs with limited budgets
  Pix4D is $292-$350/mo -OR- $4,990 one-time
  ODM is $0* (free forever)
But equally important:
Control over your toolchain (change if you want)
Shoulders of giants: many contributors, collective wisdom
Transparency leads to greater
  Quality
  Security
*You can pay for certain parts, but not required.

## Slide 6: ODM History
End of 2013 - Began as a joke on Geohipster
End of 2014 - Funded, organized FOSS project with multiple contributors
2015-2018 - Quietly expanded and refined tools and workflow
2018-2020 - Significant UI/ feature improvements, wider adoption
Today - Active community of international users, contributors

## Slide 7: ODM Goals
Humanitarian
Ecology, conservation
Research
Data for the public good

## Slide 8: The Process

## Slide 9: ODM and the Photogrammetric Process
Structure from Motion
Point Cloud Densification
Poisson Surface Reconstruction
Multi-View Stereo Texturing
Orthophoto Generation

## Slide 10: Structure from Motion
Matches features extracted from images with overlap
Image: Michelle Tobias

## Slide 11
Image: https://geokota.wordpress.com/

## Slide 12: ODM and the photogrammetric process
Structure from Motion
Point Cloud Densification
Poisson Surface Reconstruction
Multi-View Stereo Texturing
Orthophoto Generation

## Slide 13: Sparse Point Cloud from Matching
Image: opendronemap.org
Notes: (Photogrammetrically Derived Point Cloud)

## Slide 14: Dense Point Cloud
Image: opendronemap.org

## Slide 15: ODM and the photogrammetric process
Structure from Motion
Point Cloud Densification
Surface Reconstruction
Multi-View Stereo Texturing
Orthophoto Generation

## Slide 16: Mesh
Image: opendronemap.org
Notes: Uses the Point Cloud Library (PCL), followed by mesh decimation

## Slide 17: Mesh
Image: opendronemap.org
Notes: Uses the Point Cloud Library (PCL), followed by mesh decimation

## Slide 18: ODM and the photogrammetric process
Structure from Motion
Point Cloud Densification
Surface Reconstruction
Multi-View Stereo Texturing
Orthophoto Generation

## Slide 19: Texturing
Image: opendronemap.org

## Slide 20: ODM and the photogrammetric process
Structure from Motion
Point Cloud Densification
Surface Reconstruction
Multi-View Stereo Texturing
Orthophoto Generation

## Slide 21: Orthophoto
Image: opendronemap.org

## Slide 22: Use Cases

## Slide 23: Construction
Drone with a standard (RGB) camera
Capture weekly images of construction site
Use ODM to generate orthophoto, 3D model
Use ODM linear, area, and volume measurements
Monitor as-built progress against plans
Updates to owners and other stakeholders
Image: Stephen Mather

## Slide 24: Agriculture
Drone with multispectral camera
Capture biweekly images of a large field
Use ODM plant health algorithms
Visually monitor crop health
Highlight areas of plant stress, for focused attention
Image: community.opendronemap.org

## Slide 25: Emergency Management
Drone with standard camera
Quickly map a levee breach / flood area
Identify and quantify damage areas
Prioritize resources, work
Measure volume of fill material needed
Repeat flights to monitor progress
Image: opendronemap.org

## Slide 26: Coastal Monitoring
Drone with standard camera
Capture photos of a section of coastline
Use ODM to generate a 3D model
Repeat every 3 months
Export 3D models
Use another tool (e.g., CloudCompare) to assess change over time
Image: Stephen Mather

## Slide 27: Using ODM

## Slide 28: Supported Systems
Windows 10 (+ Docker)
Ubuntu Linux (native, or Docker)
MacOS

## Slide 29: Ways to Use ODM
WebODM – most common
  Manual (free)
  Installer ($)
WebODM Lightning – easiest
  Process on Lightning servers ($)
Command Line ODM
API (NodeODM)
LiveODM (USB or DVD) ($)
Portable OpenStreetMap (POSM)
Diagram: opendronemap.org

## Slide 30: Dashboard

## Slide 31: Add Images

## Slide 32: Add GCP (optional)
Built-in interface, or
GCP Editor Pro (external)
Include gcp_list.txt with images
See https://docs.opendronemap.org/gcp.html
gcp_list.txt

## Slide 33: Set Configuration

## Slide 34: Processing

## Slide 35: Finished

## Slide 36: Split/Merge for Large Datasets
Diagram: opendronemap.org

## Slide 37: Hands-On with ODM
(Part A - Start Processing)

## Slide 38: Download Sample Data
https://github.com/coreysnipes/drone_dataset_brighton_beach

## Slide 39: Unzip Files

## Slide 40: Open WebODM Lightning

## Slide 41: Add Images

## Slide 42: Add Images

## Slide 43: Set Configuration

## Slide 44: Set Configuration

## Slide 45: Set Configuration

## Slide 46: Start Processing

## Slide 47: Processing Status

## Slide 48: Running

## Slide 49: Hands-On with ODM
(End of Part A)

## Slide 50: Outputs

## Slide 51: 2D Ortho

## Slide 52: 2D Orthophoto
Overlay on Google Map, OpenStreetMap, etc
Measurements (linear, area, volume)
Contour Lines

## Slide 53: Plant Health Index
Images from multi-spectral cameras (Micasense, Sentera, etc)
Wavelengths beyond visible spectrum
Algorithms: NDVI, RDVI, GLI, SAVI, more

## Slide 54: 2D Surface Model (DSM)
Highlights surface altitude
Adjustable color ramps
Export GeoTIFF

## Slide 55: 2D Terrain Model (DTM)
“The DSM without the trees”
Uses point classification to remove objects from the surface model
Ground (terrain) profile
Contour lines

## Slide 56: 2D Terrain Model (DTM)
DTM
DSM
Images: opendronemap.org

## Slide 57: 3D Model

## Slide 58: Point Cloud
Individual points
X, Y, Z
Image: opendronemap.org

## Slide 59: Textured Model
Identify surface triangles
Point Cloud -> Surface Mesh
Image: opendronemap.org

## Slide 60: 3D Measurements
Linear
Area
Angle
Height
Height Profile
Volume

## Slide 61: Download
Orthophoto (GeoTIFF or Tiles)
Terrain Model / DTM (GeoTIFF or Tiles)
Surface Model / DSM (GeoTIFF or Tiles)
3D Point Cloud (.laz)
3D Textured Model (.obj)
Camera Parameters

## Slide 62: Output Quality
Comparable to commercial products
Commercial output quality can be better with:
  Default settings
  Poor flight coverage
ODM produces comparable quality with:
  Sometimes with default settings
  Often with tuned settings
  Good flight coverage (overlap, multiple POV)
https://opendronemap.github.io/UAVArena/

## Slide 63: Pitfalls

## Slide 64: Common Problems
Many paths to get started with ODM.
  Where to start?
  All require some work
Starting with a large dataset
System resources
  Machine spec
  Docker allocations
Processing is hung (or is it?)
Processing failed, but not sure why
Output quality vs. expectation

## Slide 65: Future Direction

## Slide 66: Upcoming Features
Reporting statistics
GPU support
Processing speed improvements
Thermal images support
Supplemental images from ground- and 360-cameras

## Slide 67: Summary

## Slide 68: Summary
ODM is a set of tools for 2D mapping and 3D modeling
ODM is Open Source, with benefits in
  Cost
  Control
Uses
  Site assessment
  Site monitoring
  Disaster response
  Construction, agriculture, mapping

## Slide 69: Summary, Continued
2D outputs
  Orthophoto
  Terrain/Surface Models
  Plant Health
3D outputs
  Point cloud
  Textured mesh
Complex to start, can be fiddly to use
Output quality is comparable to commercial software
Community has momentum

## Slide 70: Learning More

## Slide 71: ODM Docs
https://docs.opendronemap.org

## Slide 72: ODM Book
https://odmbook.com
$30
Image: odmbook.com

## Slide 73: UAV Arena
Compare Outputs
  ODM
  Pix4D
  DroneDeploy
  Agisoft Metashape
  DroneMapper
https://opendronemap.github.io/UAVArena/

## Slide 74: Community Forum
https://community.opendronemap.org

## Slide 75: Questions?
Corey’s Contact Info
@coreysnipes
corey@twomile.com
https://www.linkedin.com/in/coreysnipes/
Presentation Credits
Stephen Mather ODM, Cleveland Metroparks
Piero Toffanin ODM, UAV4GEO
https://opendronemap.org
Screenshots and interface images by
Corey Snipes, unless otherwise noted.

## Slide 76: Q&A / Break
(~15 minutes)

## Slide 77: Hands-On with ODM
Part B – Working with ODM Outputs

## Slide 78: WebODM vs. WebODM Lightning
WebODM
  Install for free
  Process locally for free
WebODM Lightning
  Commercial service
  Install for free
  Process in the cloud ($)

## Slide 79: Still Running?

## Slide 80: Finished
Today, Speed > Quality

## Slide 81: Exercises – 2D Orthophoto

## Slide 82: #1 – Orthophoto - Navigate
Click+hold = move map
Scroll wheel = zoom in/out
Map controls +/- = zoom
Map control square = full screen
Top buttons:
  Ortho
  Plant Health
  Surface Model
  Terrain Model

## Slide 83: #2 – Orthophoto - Measure
Click ruler (4th on right)
Create new measurement
Click 2 points on map
Click “Finish measurement”
View calculations in white balloon
Close balloon with “x”
Click ruler again, new measurement
Click 4 points on map to make a box, click “Finish”
View calculations
Click “Delete” to remove it

## Slide 84: #3 – Plant Health
2nd Top Button: Plant Health
Note color differences in different grassy areas
Click top right “layers” icon
View “Algorithm” options
View “Color” options
Drag min/max bars
Export GeoTIFF

## Slide 85: #4 – Surface Model (DSM)
3rd Top Button: Surface Model
Wait for calc/load
Note color varies by altitude
Click top right “layers” icon
View “Color” options
Drag min/max bars
Wait for refresh
Export GeoTIFF

## Slide 86: #5 – Terrain Model (DTM)
4th Top Button: Terrain Model
Wait for calc/load
Note color varies by altitude
Click top right “layers” icon
View “Color” options
Drag min/max bars
Wait for refresh
Export GeoTIFF

## Slide 87: Exercises – 3D Model

## Slide 88: #6 – 3D Model - Navigate
Left click+drag = rotate model
Right click+drag = move model
Scroll wheel = zoom in/out
Top left (3 bars) button = collapse tools
Top left (map) button = show model location
Tools
  Measure
  Navigation
Appearance
Scene

## Slide 89: #7 – 3D Model – Measure (Linear)
Adjust the model so you can see
Click 3rd Measurement tool (angled line)
LEFT click 2 points in a grassy area on the map
Now RIGHT click the last point to finish
View measured distance (m)
Click red “X” in measurement tools, to delete

## Slide 90: #8 – 3D Model – Measure (Area)
Adjust the model so you can see
Click top right Measurement tool (red box)
LEFT click 4 points in a grassy area on the map
Now RIGHT click the last point to finish
View measured distances (white)
View measured area (green)

## Slide 91: #9 – View Textured Model
Find “Textured Model” near the top of the tool menu
Click to expand, then click “Show Model”
Wait a few seconds
View how the scene becomes more detailed, holes are filled
Uncheck and check the box to turn off, and on
Move the model around to view other parts
Edges of model = lots of error Interior of model = better precision

## Slide 92: #10 – View Cameras
Find “Cameras” near the top of the tool menu
Click to expand, then click “Show Cameras”
Zoom out (scroll) until you see the blue squares floating above the scene
Note positions, angles of cameras
Click one camera to see the photo from that position

## Slide 93: Exercises – Download

## Slide 94: #11 – Download Orthophoto

## Slide 95: #12 – Download All

## Slide 96: Hands-On with ODM
(End of Part B)

## Slide 97: Questions?
Corey’s Contact Info
@coreysnipes
corey@twomile.com
https://www.linkedin.com/in/coreysnipes/
Presentation Credits
Stephen Mather ODM, Cleveland Metroparks
Piero Toffanin ODM, UAV4GEO
https://opendronemap.org
Screenshots and interface images by
Corey Snipes, unless otherwise noted.

## Slide 98: Backup