## Slide 1: Open Source Data Processing with OpenDroneMap
Corey Snipes
DroneCamp
July 28, 2021

## Slide 2: Agenda
Background
Hands-On: Start Processing
Outputs
Using ODM
Learning Resources
Hands-On: Exercises

## Slide 3
Background

## Slide 4: About Me
Aviation Software Engineer
Part 107 Remote Pilot
North Coast Drone Alliance
OpenDroneMap Contributor
UN OpenGIS ODM Expert Group

## Slide 5: What is ODM?
Open-source toolkit for photogrammetry from UAS imagery and sensor data
Georeferenced 2D and 3D outputs
  Orthophoto, DSM, DTM
  Point Cloud, Textured Mesh
Used globally by universities and research programs
Used by the Red Cross, World Bank, United Nations
Begun in 2014, significant improvements 2018-2021
  Output Quality
  Features
  Usability

## Slide 6: Why Open Source?
FOSS is popular in academic and research settings, but why?
Accessible to orgs and programs with limited budgets
  Pix4D is $292-$350/mo -OR- $4,990 one-time
  ODM is $0* (free forever)
But equally important:
Control over your toolchain (change if you want)
Shoulders of giants: many contributors, collective wisdom
Transparency leads to greater
  Quality
  Security
*You can pay for certain parts, but not required.

## Slide 7: ODM History
End of 2013 - Began as a joke on Geohipster
End of 2014 - Funded, organized FOSS project with multiple contributors
2015-2018 - Quietly expanded and refined tools and workflow
2018-2021 - Significant UI/ feature improvements, wider adoption
Today - Active community of international users, contributors

## Slide 8: ODM Goals
Humanitarian
Ecology, conservation
Research
Data for the public good

## Slide 9
Hands-On: Part A
Start Processing

## Slide 10: Download Sample Data
https://github.com/pierotofy/drone_dataset_sheffield_park_1/tree/master

## Slide 11: Unzip Files

## Slide 12: Remove LICENSE.md file

## Slide 13: Open WebODM Lightning

## Slide 14: Add Images

## Slide 15: Add Images
(No Ground Control Points, today)

## Slide 16: Set Configuration

## Slide 17: Set Configuration

## Slide 18: Set Configuration

## Slide 19: Start Processing

## Slide 20: Processing Status

## Slide 21: Running

## Slide 22
Outputs

## Slide 23: 2D Ortho

## Slide 24: 2D Orthophoto
Overlay on Google Map, OpenStreetMap, etc
Measurements (linear, area, volume)
Contour Lines
   QGIS/ArcGIS
   Object detection/counting via FieldMapR, rastervision.io

## Slide 25: Plant Health Index
Images from multi-spectral cameras (Micasense, Sentera, etc)
Wavelengths beyond visible spectrum
Algorithms: NDVI, RDVI, GLI, SAVI, more

## Slide 26: 2D Surface Model (DSM)
Highlights surface altitude
Adjustable color ramps
Export GeoTIFF

## Slide 27: 2D Terrain Model (DTM)
“The DSM without the trees”
Uses point classification to remove objects from the surface model
Ground (terrain) profile
Contour lines

## Slide 28: 2D Terrain Model (DTM)
DTM
DSM
Images: opendronemap.org

## Slide 29: 3D Model

## Slide 30: Point Cloud
Individual points
X, Y, Z
Measurements
Image: opendronemap.org
   CloudCompare for analysis

## Slide 31: Textured Model
Identify surface triangles
Point Cloud -> Surface Mesh
Image: opendronemap.org
   Sketchfab, et al for sharing
   CAD, Blender
   3D print

## Slide 32: 3D Measurements
Linear
Area
Angle
Height
Height Profile
Volume

## Slide 33: Download
Orthophoto (GeoTIFF)
Terrain Model / DTM (GeoTIFF)
Surface Model / DSM (GeoTIFF)
3D Point Cloud (.laz)
3D Textured Model (.obj)
Camera Parameters
Quality Report
Everything (all.zip)

## Slide 34
Using ODM

## Slide 35: Supported Systems
Windows 10 (Docker, or native)
Ubuntu Linux (Docker, or native)
MacOS
16+ GB RAM (more is better)
50+ GB Disk (more is better)

## Slide 36: Ways to Use ODM
WebODM – most common
  Manual (free)
  or, Installer ($)
WebODM Lightning – easiest
  Process on Lightning servers ($)
Command Line ODM
API (NodeODM)
LiveODM (USB or DVD) ($)
Portable OpenStreetMap (POSM)
Diagram: opendronemap.org

## Slide 37: Common Problems
Many paths to get started with ODM.
  Where to start?
  All require some work
Jumping in with a large dataset (start small!)
System resources
  Machine spec
  Docker allocations
Processing is hung (or is it?)
Processing failed, but not sure why
Output quality vs. expectation

## Slide 38: Large Datasets
Split/Merge
ClusterODM
Diagram: opendronemap.org

## Slide 39: Output Quality
Comparable to commercial products
Commercial output quality can be better with:
  Default settings
  Poor flight coverage
ODM produces comparable quality with:
  Sometimes with default settings
  Often with tuned settings
  Good flight coverage (overlap, multiple POV)
https://opendronemap.github.io/UAVArena/

## Slide 40: Object Detection, Counting, Analysis
Documented workflows using external tools (not within ODM)
FIELDimageR
  “A Tool to Analyze Orthomosaic Images From Agricultural Field Trials in R”
  https://www.opendronemap.org/fieldimager/
rastervision.io

## Slide 41
Summary

## Slide 42: Output Summary
2D outputs
  Orthophoto
  Terrain/Surface Models
  Plant Health
3D outputs
  Point cloud
  Textured mesh

## Slide 43: ODM Summary
ODM is Open Source, with benefits in
  Cost
  Control
Complex to start, can be fiddly to use
Output quality is comparable to commercial software
Community has momentum

## Slide 44
Learning More

## Slide 45: UAV Arena
Compare Outputs
  ODM
  Pix4D
  DroneDeploy
  Agisoft Metashape
  DroneMapper
https://opendronemap.github.io/UAVArena/

## Slide 46: ODM Docs
https://docs.opendronemap.org

## Slide 47: ODM Book
https://odmbook.com
$30
Image: odmbook.com

## Slide 48: Community Forum
https://community.opendronemap.org

## Slide 49
Hands-On: Part B
Working with Outputs

## Slide 50: WebODM vs. WebODM Lightning
WebODM
  Install for free
  Process locally for free
WebODM Lightning
  Commercial service
  Install for free
  Process in the cloud ($)

## Slide 51: Still Running?

## Slide 52: Finished
Today, Speed > Quality

## Slide 53: Exercises – 2D Orthophoto

## Slide 54: #1 – Orthophoto - Navigate
Click+hold = move map
Scroll wheel = zoom in/out
Map controls +/- = zoom
Map control square = full screen
Top buttons:
  Ortho
  Plant Health
  Surface Model
  Terrain Model

## Slide 55: #2 – Orthophoto - Measure
Click ruler (5th on right)
Create new measurement
Click 2 points on map
Click “Finish measurement”
View calculations in white balloon
Close balloon with “x”
Click ruler again, new measurement
Click 4 points on map to make a box, click “Finish”
View calculations
Click “Delete” to remove it

## Slide 56: #3 – Plant Health
2nd Top Button: Plant Health
Note color differences in different grassy areas
Click top right “layers” icon
View “Algorithm” options
View “Color” options
Drag min/max bars
Export GeoTIFF

## Slide 57: #4 – Surface Model (DSM)
3rd Top Button: Surface Model
Wait for calc/load
Note color varies by altitude
Click top right “layers” icon
View “Color” options
Drag min/max bars
Wait for refresh
Export GeoTIFF

## Slide 58: #5 – Terrain Model (DTM)
4th Top Button: Terrain Model
Wait for calc/load
Note color varies by altitude
Click top right “layers” icon
View “Color” options
Drag min/max bars
Wait for refresh
Export GeoTIFF

## Slide 59: Exercises – 3D Model

## Slide 60: #6 – 3D Model - Navigate
Left click+drag = rotate model
Right click+drag = move model
Scroll wheel = zoom in/out
Top left (3 bars) button = collapse tools
Top left (map) button = show model location
Tools
  Measure
  Navigation
Appearance
Scene

## Slide 61: #7 – 3D Model – Measure (Linear)
Adjust the model so you can see
Click 3rd Measurement tool (angled line)
LEFT click 2 points on the map
Now RIGHT click the last point to finish
View measured distance (m)
Click red “X” in measurement tools, to delete

## Slide 62: #8 – 3D Model – Measure (Area)
Adjust the model so you can see
Click top right Measurement tool (red box)
LEFT click 4 points on the map
Now RIGHT click the last point to finish
View measured distances (white)
View measured area (green)

## Slide 63: #9 – View Textured Model
Find “Textured Model” near the top of the tool menu
Click to expand, then click “Show Model”
Wait a few seconds
View how the scene becomes more detailed, holes are filled
Uncheck and check the box to turn off, and on
Move the model around to view other parts
Edges of model = lots of error Interior of model = better precision

## Slide 64: #10 – View Cameras
Find “Cameras” near the top of the tool menu
Click to expand, then click “Show Cameras”
Zoom out (scroll) until you see the blue squares floating above the scene
Note positions, angles of cameras
Click one camera to see the photo from that position

## Slide 65: Exercises – Download

## Slide 66: #11 – Download Specific Outputs

## Slide 67: #12 – Download All

## Slide 68
Thank You!
Contact Me
corey@twomile.com
https://www.linkedin.com/in/coreysnipes
This material is based on presentations by:
Stephen Mather - ODM, Cleveland Metroparks
Piero Toffanin - ODM, UAV4GEO
https://opendronemap.org
Screenshots and interface images by
Corey Snipes, unless otherwise noted.
coreysnipes
twomileheavy

## Slide 69
Backup