## Slide 1
Stephen Mather, GIS Manager, Cleveland Metroparks
@smathermather, svm@clevelandmetroparks.com
Dakota Benjamin, Geospatial Developer, Cleveland Metroparks
dmb2@clevelandmetroparks.com
http://tinyurl.com/odm-inaware

## Slide 2: Outline
Introduction to OpenDroneMap
  Break
Using OpenDroneMap
  Break
Using Data from OpenDroneMap
http://tinyurl.com/odm-inaware

## Slide 3
OpenDroneMap is an open source toolkit for aerial drone imagery.
It is modern photogrammetry - fully automated matching, digital surface modeling, and mosaicking

## Slide 4: https://tinyurl.com/opendronemap

## Slide 5
OpenDroneMap is an open source toolkit for aerial drone imagery.
It is modern photogrammetry - fully automated matching, digital surface modelling, and mosaicking
Platform vs. Toolkit

## Slide 6: Origins
Computer Vision
Photogrammetry
Notes: OpenDroneMap originates from Computer Vision, i.e. how do we enable computers to navigate and understand the world.
It depends on stereo vision much like we do to make sense of the world in 3D

## Slide 7: Purposes
Ecology
Humanitarian
Participatory creation of data for the public good
http://image0-rubylane.s3.amazonaws.com/shops/suzanstreasures/VCx20-x201402.1L.jpg
Notes: OpenDroneMap originates from Computer Vision, i.e. how do we enable computers to navigate and understand the world.
It depends on stereo vision much like we do to make sense of the world in 3D

## Slide 8: ODM and the photogrammetric process
Structure from Motion
Point Cloud Densification
Poisson Surface Reconstruction
Multi-View Stereo Texturing
Orthophoto Generation

## Slide 9: ODM and the photogrammetric process
Structure from Motion
Point Cloud Densification
Poisson Surface Reconstruction
Multi-View Stereo Texturing
Orthophoto Generation

## Slide 10: Structure from Motion
Matches features extracted from images with overlap
Credit: Michelle Tobias

## Slide 11: Photogrammetry Process
Structure from Motion
Point Cloud Densification
Poisson Surface Reconstruction
Multi-View Stereo Texturing
Orthophoto Generation

## Slide 12: Point Cloud from Matching
Notes: (Photogrammetrically Derived Point Cloud)

## Slide 13: Dense Point Cloud from finding all matches

## Slide 14: Photogrammetry Process
Structure from Motion
Point Cloud Densification
Poisson Surface Reconstruction
Multi-View Stereo Texturing
Orthophoto Generation

## Slide 15: Mesh
Notes: Uses the Point Cloud Library (PCL), followed by mesh decimation

## Slide 16: Mesh
Notes: Uses the Point Cloud Library (PCL), followed by mesh decimation

## Slide 17: Photogrammetry Process
Structure from Motion
Point Cloud Densification
Poisson Surface Reconstruction
Multi-View Stereo Texturing
Orthophoto Generation

## Slide 18: Texturing

## Slide 19: Photogrammetry Process
Structure from Motion
Point Cloud Densification
Poisson Surface Reconstruction
Multi-View Stereo Texturing
Orthophoto Generation

## Slide 20: Orthophoto Generation

## Slide 21: How to Use OpenDroneMap

## Slide 22: Usage
Command line tool
Portable OpenStreetMap (POSM)
WebODM
API
  API Docs: https://opendronemap.github.io/WebODM/

## Slide 23: Installation
There are many ways to install ODM:
  Natively using Ubuntu 14.04 or later (or with Virtual Machine via vagrant)
  Linux, MacOS or Windows, by installing Docker
  Via the above methods but with a Web-based GUI called WebODM

## Slide 35: Funding and Future

## Slide 36: Funding
Cleveland Metroparks
American Red Cross
  Integration with Portable OpenStreetMap (POSM)
Humanitarian Innovation Fund
  Make ODM Easier to Use
  Make the products from it better / more accurate
Others?

## Slide 37: OpenDroneMap: Future
Quality and robustness improvements
Scalability
  Reduce memory footprint
  Data Partitioning
Analysis
  Add automated DTM extraction
  Classification
Mesh improvements

## Slide 38: DTM Extraction
Near future

## Slide 39
Midpines, flown by NextGen Air Transportation Center (NGAT) access to the data through collaboration with Center for Geospatial Analytics at NCSU

## Slide 40
Midpines, flown by NextGen Air Transportation Center (NGAT) access to the data through collaboration with Center for Geospatial Analytics at NCSU

## Slide 41
Midpines, flown by NextGen Air Transportation Center (NGAT) access to the data through collaboration with Center for Geospatial Analytics at NCSU

## Slide 42: Near-term improvements
Quality reporting and robustness improvements
Incremental optimizations
Large-scale pipeline

## Slide 43: Quality reporting and robustness improvements
Add reporting system to OpenSfM
  Collect metadata on Structure from Motion Process
    Number of matches, Matching graph between images, Number of reconstructed images and points, Histogram of reprojection errors, Memory Usage, etc.
Improve Robustness
  Analyze and classify failures
  Improve results on difficult datasets
  Establish test datasets for ongoing testing

## Slide 44: Large-scale pipelineor breaking datasets into bite-size pieces
Split large numbers of images into smaller groups
Run OpenSfM reconstruction on each subgroup
Align and transform those groups to each other using matching features between the groups

## Slide 45: Large-scale pipelineor breaking datasets into bite-size pieces

## Slide 46: Incremental optimizations or what happens after it’s down the gullet
Improve processor use
  Cascade Hashing1 matching
    or
  Bag of Words2
Improved Memory Use:
  Improved correspondence graph data structures
  SLAM-like pose-graph methods for global adjustment of camera position
[1] Jian Cheng, Cong Leng, Jiaxiang Wu, Hainan Cui, Hanqing Lu; The IEEE Conference on Computer Vision and Pattern Recognition (CVPR), 2014, pp. 1-8
[2] Michal Havlena, Konrad Schindler; VocMatch: Efficient Multiview Correspondence for Structure from Motion; Institute of Geodesy and Photogrammetry, ETH Zurich, Switzerland

## Slide 47: WebODM: Future
DEM display
Volumetric Measurements
Mission Planning
Mobile App for autonomous flight
QGIS integration
Integration with Entwine + Greyhound
Integration with OpenAerialMap

## Slide 48
Stephen Mather, GIS Manager, Cleveland Metroparks
@smathermather, svm@clevelandmetroparks.com
Dakota Benjamin, Geospatial Developer, Cleveland Metroparks
dmb2@clevelandmetroparks.com
http://tinyurl.com/odm-inaware

## Slide 49: Outline
Introduction to OpenDroneMap
  Break
Using OpenDroneMap
  Break
Using Data from OpenDroneMap
http://tinyurl.com/odm-inaware

## Slide 50: Outline
Using OpenDroneMap
  Command-line use
  Docker Use
  WebODM Use
http://tinyurl.com/odm-inaware

## Slide 51: Installation Instructions
https://github.com/OpenDroneMap/OpenDroneMap

## Slide 52: Installation and Command-line Use
Download the latest release:
  https://github.com/OpenDroneMap/OpenDroneMap/releases
Extract and enter the OpenDroneMap directory
Run bash configure.sh
Download and extract a sample dataset:
  https://github.com/OpenDroneMap/odm_data_aukerman/archive/master.zip
Run ./run.sh --project-path <PATH>, replacing <PATH> with the dataset path.

## Slide 53: Docker Use
cd directory_path
docker run -it --rm -v $(pwd)/images:/code/images /
-v $(pwd)/odm_orthophoto:/code/odm_orthophoto /
-v $(pwd)/odm_texturing:/code/odm_texturing /
opendronemap/opendronemap

## Slide 54
Stephen Mather, GIS Manager, Cleveland Metroparks
@smathermather, svm@clevelandmetroparks.com
Dakota Benjamin, Geospatial Developer, Cleveland Metroparks
dmb2@clevelandmetroparks.com
http://tinyurl.com/odm-inaware

## Slide 55: Outline
Introduction to OpenDroneMap
  Break
Using OpenDroneMap
  Break
Using Data from OpenDroneMap
http://tinyurl.com/odm-inaware

## Slide 56: Outline
Using Data from OpenDroneMap
  Downloading assets
  Loading in QGIS
  Loading in meshlab
  Loading in pdal.io
http://tinyurl.com/odm-inaware

## Slide 57
Stephen Mather, GIS Manager, Cleveland Metroparks
@smathermather, svm@clevelandmetroparks.com
Dakota Benjamin, Geospatial Developer, Cleveland Metroparks
dmb2@clevelandmetroparks.com
http://tinyurl.com/odm-inaware